DVX100 Setup and Usage

9/10/2013 2:53 PM by Glenn Meader

# DVX100 Setup Checklist

( Initialize the user file (resets all items except the scene files)

MENU button. Choose 7. OTHER FUNCTIONS, select USER FILE (10th item down), select YES, select INITIAL, select YES. The settings for the current user file are returned to the factory settings. (see DVX100B Manual Page 78)

## ( Initialize the scene files

From the 6 scene files, select the one you want to initialize with the scene dial (F1). Press MENU button, select 1. SCENE FILE, SAVE/INIT (16th item down), YES, select INITIAL, YES. The settings for the selected scene file are returned to the factory settings. (Page 70) There is no effect on the other scene files.

## ( Set Scene Dial

Set scene dial to F1 (normal)

## ( Set Viewfinder diopter

Dial on the side of the viewfinder. (Page 23)

## ( Set Clock

- MENU button, 7. OTHER FUNCTIONS, CLOCK SET, YES

- Use (( ((buttons to change value

- Use (( to select item to change

## ( Audio/Microphone

Set input select switches for CH1 and CH2 to INT for internal mic.
Turn off ALC if you are actively checking audio levels (preferred). MENU button, 5. RECORDING SETUP, MIC ALC (3rd item).
If using external mic or line feed, set Mic/Line switch and input select switches.

## ( Battery

Use a fully charged battery. Keep a spare battery with you. (Page 21) Batteries last about 5 hours and take about 5½ hours to recharge.

## ( Cassette tape

Check that the cassette tape can be used for recording.

• Make sure the green erasure prevention tab on the tape is set to REC.

• Make sure the tape doesn’t have images you want to keep recorded on it.

• Make sure the cassette holder is completely closed.  (Pages 10 and 15)

Optionally set the camera recording speed to LP (90 minutes) default is SP (60 minutes)

## ( Zoom, focus, and iris

• Check that motor-driven zooming is possible. (Page 32)

• Check that the focusing can be performed both automatically and manually. (Page 38)

• Check that the lens iris operations can be performed automatically and manually. (Page 43)

## Charge internal battery

If internal battery (stores settings) is low, connect to AC adapter, turn off camera, wait 4 hours.

# DVX100 Usage Notes

## Auto/Manual

Press Auto button to toggle Auto/Manual mode. A in a ( box icon appears in viewfinder to indicate Auto mode. The camera makes the following adjustments automatically for you when in auto mode:
• Focus • Gain • Iris • White balance

## Focus

AFnn or MFnn shows percentage of focus range on screen (Auto or Manual).

Use the FOCUS switch to choose focus mode.

- A (AUTO): Auto focus mode

- M (MANUAL): Manual focus mode Turn the focus ring by hand.

- ∞ : The camera focuses on infinity, then it reverts to manual focus.

Temporarily switching to auto focus Even if you have switched FOCUS to M (MANUAL) the camera will focus automatically while you press down PUSH AUTO.

## Zoom

Znn shows the percentage of zoom on the screen.

Zoom button

Set the ZOOM switch to SERVO so that you can use the motor-driven zoom. T: Zoom in W: Zoom out Gently press the zoom button above the tape door to zoom slowly, firmly press to zoom faster. You can change the zoom speed on the handle zoom button by selecting one of three speeds with the HANDLE ZOOM switch. Set HANDLE ZOOM switch speeds by going to the setup menus, SW MODE screen HANDLE ZOOM. (Page 71)

Zoom ring

Set the ZOOM switch to MANU so that you can use the zoom ring. You cannot rotate the zoom ring if the ZOOM switch is set to SERVO. Trying to use it could damage the camera.

## EVF DTL

Emphasizing the outlines of the images you see in the viewfinder or on the LCD makes it easier to focus. Press EVF DTL/END SEARCH to toggle the EVF DTL on and off.

## Zebra

Press the ZEBRA button in the camera mode to show the zebra pattern or marker on the screen so you can check the brightness of the subject. Parts that may be whited out through over exposure are shown as a zebra pattern. You can remove most overexposed parts by adjusting the iris and shutter speed in the manual mode to remove the areas with zebra patterns.

## User buttons

Use these buttons to change shooting settings quickly or add effects to the images you are shooting. The following features are allocated to the buttons at the time of shipping.

USER1: COLOR BAR This feature to outputs a color bar screen to a television or monitor so you can adjust them.

USER2: BACKLIGHT Use this feature when shooting subjects lit from the back. BACK appears on the screen. Backlight compensation adjusts the iris so the subject doesn’t come out dark.

USER3: INDEX Use this feature during shooting to record an index signal to the tape. Adding indexes means that you can make index searches during play.(Page 50)

## Optical Image Stabilizer

Use the Optical Image Stabilizer (OIS) to reduce the effects of camera shake when shooting by hand. Press the OIS button to turn the function on and off. A hand icon appears on the screen when this function is on. Turn the function off when using a tripod for more natural images.

## White balance

White balance is automatically controlled in Auto (focus) mode.

In manual mode you control the white balance. Aim at a white card and press the AWB button. Or set the WHITE BAL switch to PRST to use the two preset color temp options. Press the AWB button to switch between 3200 K (halogen) and 5600 K (outdoor).

## Intensity

When in Manual mode, switch the image gain with the GAIN switch. L: Set Low (normal) gain M: set Medium gain H: Set High gain

Use the ND FILTER Switch to change the ND Filter used (filter to change light intensity).

- OFF: ND filter is not used.

- 1/8: Cuts light intensity by up to about 1/8.

- 1/64: Cuts light intensity by up to about 1/64.

## Iris

The iris is automatically controlled in manual (focus) mode.

Press the IRIS button to switch how to adjust the aperture of lens. AUTO IRIS: Adjust the iris automatically. MANUAL IRIS: Adjust the iris manually. Turn the IRIS dial to adjust the aperture of lens when in the manual iris mode. • Even if Auto IRIS is used, you can correct the aperture with this dial.

## LCD backlight

In MENU, 6. DISPLAY SETUP, LCD BACKLIGHT (10th item) – can set the backlight to HI (to view better in sunlight)

## Rec Check button

While in the shooting standby mode, press the REC CHECK button. A few seconds of the last thing you shot play, and then the camera returns to the shooting standby mode.

## Playback

Press CAMERA/VCR button so green LED glows. Use toggle switch near MENU button to control VCR.